## Slide 1: SDNFV FINAL PROJECT
SDN Network as Virtual Router
助教：蔣汶儒
sdnta@win.cs.nycu.edu.tw
Deadline: 2024/12/19

## Slide 2: OUTLINE
Review of Labs
Virtual Router Explained
Virtual Router Specification
ONOS App and Services in Use
In Used App Configurations
Virtual Router Workflow
Project Information and Installation
Supplement
Scoring Criteria
Reference

## Slide 3: OUTLINE
Review of Labs
Virtual Router Explained
Virtual Router Specification
ONOS App and Services in Use
In Used App Configurations
Virtual Router Workflow
Project Information and Installation
Supplement
Scoring Criteria
Reference

## Slide 4: Review of Labs
Lab2
  ONOS API
  Flow rules
Lab3
  Mac learning
  Proxy ARP
Lab4
  Intent
  Meter Table
Lab5 Network Function Virtualization
  Simulate Autonomous Systems (AS)

## Slide 5: OUTLINE
Review of Labs
Virtual Router Explained
Virtual Router Specification
ONOS App and Services in Use
In Used App Configurations
Virtual Router Workflow
Project Information and Installation
Supplement
Scoring Criteria
Reference

## Slide 6: SDN-enabled Virtual Router
SDN Network with virtual router
  Use openflow switches and flowrules to simulate router behavior
  For instance:
    Layer2 forwarding for next hop communication
    Boarder gateway route exchange
    Etc.
SDN Network
AS 65000
AS 65001
AS 65002

## Slide 7: Traffic Types
Intra-domain Traffics
  Where hosts within the same AS communicates with each other.
  SDN handles the traffic.
SDN Network
AS 65000
AS 65001
AS 65002

## Slide 8: Traffic Types (cont.)
Inter-domain Traffics
  Where an external host from other domain communicates with an internal host.
  The traffic pass through gateways.
  Virtual router needs to do something.
SDN Network
AS 65000
AS 65001
AS 65002

## Slide 9: Traffic Types (cont.)
Transit Traffics
  Where hosts from different domains communicates with one another bypass the SDN network.
  The traffic pass through virtual router.
  Virtual router needs to do something.
SDN Network
AS 65000
AS 65001
AS 65002

## Slide 10: Networks with Physical Routers
Physical routers
  1. Deal with routing decision.
  2. Deal with gateway exchange.
Every edge requires a router, running eBGP and iBGP protocols.
AS 65000
AS 65001
AS 65002
Switch
Switch
AS 65003

## Slide 11: SDN Networks with Virtual Routers
SDN-enabled Virtual Routers
  Doesn’t requires router connection to edge.
  Only one BGP speaker is enough.
  Doesn’t need a real gateway.
AS 65000
AS 65001
AS 65002
OVS1
OVS2
AS 65003
BGP Speaker
(FRRouting)

## Slide 12: OUTLINE
Review of Labs
Virtual Router Explained
Virtual Router Specification
ONOS App and Services in Use
In Used App Configurations
Virtual Router Workflow
Project Information and Installation
Supplement
Scoring Criteria
Reference

## Slide 13: Goal
Intra-domain host communication
  Handled by Bridge APP
Inter-domain host communication
  SDN domain <-> Other domain
Transit host communication
  Other domain <-> SDN domain <-> Other domain

## Slide 14: vRouter Specification
Intra AS packet forwarding and packet-in request
  Lab3
Arp Reply for devices in AS
  Lab3
Inter-domain eBGP traffic topology
  Lab5
Routing table maintenance
  Lab5
Flowrules for intra/inter/transit domain traffic
  vRouter APP
IPv4 and IPv6 Dual stack
  With Additional IPV6 Capability !!!!

## Slide 15: OUTLINE
Review of Labs
Virtual Router Explained
Virtual Router Specification
ONOS App and Services in Use
In Used App Configurations
Virtual Router Workflow
Project Information and Installation
Supplement
Scoring Criteria
Reference

## Slide 16: ARP in IPv6
ARP are only for IPv4s, how does IPv6 know the MAC address of the target?
Neighbor Discovery Protocol (NDP)
  ICMPv6 Messages
  Neighbor Solicitation (Type 135)
    Similar to ARP request
  Neighbor Advertisement (Type 136)
    Similar to ARP response
Type
Code
Checksum
Content
ICMPv6 Packet

## Slide 17: ARP App Extension for IPv6
Handle certain packets
Example code to determine neighbor solicitation packet type
Simple way to build a neighbor advertisement packet

## Slide 18: Virtual Router BGP Connection
Physical router:
  External routers connect with the boarder gateway.
Virtual router:
  External routers connect with BGP Speaker.
  Need to delegate BGP Speaker IP to edge switch.

## Slide 19: BGP Speaker IP Delegation and Routing
Delegate BGP speaker IP to the WAN Connect Point on edge switch.
  Determine WAN Connect Point.
  Config (via netcfg) WAN Connect Point interface.
Route packet between BGP speaker Connect Point and WAN Connect Point.
  Determine BGP speaker connect point.
  Install rule to route packets.

## Slide 20: WAN Connect Point Configuration
Create a configuration file for WAN Connect Point
  Making external routers think that the BGP Speaker is at the Connect Point.
Connect Point
Interface Config
*NOTE
This only gives ONOS controller information of the interface and its IPs. How to make BGP speaker receive packets designated to the IP is your work!

## Slide 21: WAN Connect Point Information Retrieval
Use ONOS Interface Service to retrieve WAN Connect Point.
  Import Interface service
  Reference interface service
  Query WAN Connect Point information from the interface service

## Slide 22: Zebra FIB Pushing
Zebra supports a Forwarding Information Base (FIB) Push Interface (FPI)
  FPI allows an external component to learn the forwarding information.
Forwarding Plane Manager (FPM)
  Receives FIB
  Decode FIB into routes
FIB pushing:
  FPM establishes a TCP connection with Zebra
  Zebra pushes FIB to FPM
In this project, we use ONOS built-in FPM to collect FIB from zebra.

## Slide 23: BGP Route Retrieval with Route Service
Route Service will collect route information via FPM APP.
Routes provided by Route Service contains next hop info for target subnet.
Route Service provide routing table query API.

## Slide 24: ONOS Route Service Usage
Update dependencies in pom.xml file.
Import methods.
Read the docs
https://javadoc.io/doc/org.onosproject/onos-cli/1.8.1/org/onosproject/incubator/net/routing/package-summary.html

## Slide 25: OUTLINE
Review of Labs
Virtual Router Explained
Virtual Router Specification
ONOS App and Services in Use
Zebra and FRRouting Configurations
Virtual Router Workflow
Project Information and Installation
Supplement
Scoring Criteria
Reference

## Slide 26: Enabling FPM Module
To enable FPM, you have to set –M fpm in zebra_options at /etc/frr/daemons

## Slide 27: FRRouting Configuration
Configurations in /etc/frr/frr.conf
Peer Group (template) for neighbors
Use the template
BGP Passwords
Don’t advertise the prefix that you received
Announce IPv4 prefix on IPv4 Interface
Same as IPv6 Interface
FPM connection
NOTE* Older versions of FRRouting might not work, this is just an example

## Slide 28: OUTLINE
Review of Labs
Virtual Router Explained
Virtual Router Specification
ONOS App and Services in Use
In Used App Configurations
Virtual Router Workflow
Project Information and Installation
Supplement
Scoring Criteria
Reference

## Slide 29: BGP Message Exchange
In order to exchange BGP message with neighbor router
  Neighbor discovery for L2 connectivity
    Proxy ARP APP handles ARPs and NDPs on behalf of BGP Speaker.
  L3 forwarding for BGP Messages
L3 forwarding for BGP Messages?
  Incoming
    Hint: MultiPointToSinglePoint intent
  Outgoing
    ????

## Slide 30: Virtual Gateway and Inter-domain Routing
Gateway and Routing
  Assume Gateway IP: 192.168.1.254/24
    Packets originated from 192.168.1.0/24 towards other networks
      Packet first sent to Gateway.
    Packet coming from other networks destined 192.168.1.0/24
      Packet first received by Gateway.
IP is the logical address of ultimate destination.
  But, MAC is the physical address of the next hop.

## Slide 31: Gateway Traffic Handling Example
Any packets within the domain only knows about the gateway’s MAC.
After analyzing the information (IP), it will change the according MAC and sends the packet out.
Host A
Host B
MAC
IP
R1
R2
A
R1
A
B
src
dst
R1
R2
A
B
src
dst
R2
B
A
B
src
dst
DOMAIN A
DOMAIN B

## Slide 32: Transit Traffics
Transit traffics are in fact two interdomain traffics.
DOMAIN A
Host B
R1
R2
DOMAIN B
Host C
R4
DOMAIN C
R1
R2
A
C
src
dst
R2
R4
A
C
src
dst

## Slide 33: OUTLINE
Review of Labs
Virtual Router Explained
Virtual Router Specification
ONOS App and Services in Use
In Used App Configurations
Virtual Router Workflow
Project Information and Installation
Supplement
Scoring Criteria
Reference

## Slide 34: Linux Network Brief Introduction
Network Namespaces
  Provide a way to create isolated network environments within a Linux system.
  Allow processes to have their own network stack, including interfaces, routing tables, and firewall rules.
Each Container have it’s own Network Namespace.
A network Bridge is a kernel created logical L2 switch
Veth devices, short for virtual Ethernet devices
Use veth pairs to connect Network Namespaces or Bridges together.

## Slide 35: Linux Network Brief Introduction (cont.)
Mapping to physical instruments.
Namespace = node (computer/server)
Veth pair = 2 network interface cards (NIC) that connects to each other
Bridge = switch
If you want to connect your computer to a switch
  Create a veth pair (Create 2 NIC that connects to each other)
  Connect one NIC to your namespace
  Connect the other one to your bridge
Bridge
Veth
Namespace
Veth

## Slide 36: Linux Network Brief Introduction (cont.)
Mapping to physical instruments.
Namespace = node (computer/server)
Veth pair = 2 network interface cards (NIC) that connects to each other
Bridge = switch
How to find a container’s namespace (ns)?
  Locate docker pid
  It is at file `/proc/$pid/ns/net`
Similarly you can connect two namespaces (containers) with the same mechanism.
Container
Veth
Container
Veth

## Slide 37: Ubuntu IP Command Introduction
Normally, we can use `ip netns exec` command to execute commands inside a namespace; however, it will only search ns for directories in `/var/run/netns`
Two ways to run `ip netns exec` in container namespace
  Create a soft link `ln -sfT /proc/$pid/ns/net /var/run/netns/$pid`
  Use nsenter command `nsenter -t $pid -n <command>`
Useful ip commands
  `ip link add <name> type <type>`: Create a NIC by the type.
  `ip link set <name> up`: Bring up (enable) the NIC.
  `ip address add <ip> dev <name>`: Add an ip address to the NIC.
  `ip route show`: Show current routes.
  `ip route add {<ip> | default} via {ip}: Add a route.

## Slide 38: Docker Network Namespace Introduction
Create a container named sdnfv-demo
Find the pid of the container
Make soft link so that ip netns can find container ns
Create a dummy NIC using netns command
NIC is created inside the container
Show interface information of ns
Show interface information of the container

## Slide 39: Tunnel and VXLAN
A Tunnel send data over a network by encapsulating packets within other packets.
  Commonly used to connect different networks, provide secure communication, bypass firewalls.
  Applications
    Virtual Private Networks (VPN)
    Generic Routing Encapsulation (GRE)
    Virtual Extensible LAN (VXLAN)
  Types
    Layer 2: Transmit data that is higher or equal to Layer 2
    Layer 3: Transmit data that is higher or equal to Layer 3
VXLAN (L2 Tunnel)
  Designed to help build large, scalable L2 networks over existing L3 networks

## Slide 40: Wireguard
TA will provide a Wireguard configuration file
  Remember, the last number of your IP is your ID (x)
Run the follow command to install wireguard
Copy the configuration file to wg0
Bring up the Wireguard interface
Check if Wireguard is good
  Wireguard gateway
  VXLAN Target
This is your ID (x)
This is your x
This is Wireguard gateway
Some wireguard version requires port

## Slide 41: Maximum Transmission Unit (MTU)
The largest size (in bytes) of a network packet that can be transmitted over a particular interface or network medium without fragmentation.
Default to 1500 Bytes.
What Happens if Packet Size Exceeds the MTU?
  Fragmentation
  Drop (Especially IPv6)
Suggested subtraction of MTU due to encapsulation
  VXLAN: 50 Bytes
  Wireguard: 80 Bytes

## Slide 42: Autonomous System (AS)
AS Types
Stub
Multi Homed
Transit
Internet Exchange Point

## Slide 43: ISP Characteristic
Internet Service Provider (ISP)
  A company or organization that provides individuals, enterprises, and other entities access to the internet.
Key Concepts
  Internet Access
  Internet Service
  IP Addresses
If you have been assigned an IP from NYCU
  How does the Internet world routes packets to your IP’s location?
  How does others know the way to find you in the Internet world?
Goal: A vrouter in a small ISP and that manages internet resources.

## Slide 44: ISP Service Requirements
Service requirements for customers.
  Routers to exchange other AS’s route.
  Layer 2 modification
  Packet handling
Service requirements for other ISPs.
  Packet handling
  Quality of Service (QoS)

## Slide 45: Topology
AS65xx0 (SDN Network)
ONOS
VXLAN
FRRouting
Host 1
VXLAN
AS65000
AS65xx1
Host 2
AS65yy1
Host 2
AS65yy0 (SDN Network)
ONOS
VXLAN
Host 1
FRRouting
TA
1Gbps Rate Limit
1Gbps Rate Limit
Student y
Student x

## Slide 46: Topology for 3 Students
VXLAN
VXLAN
VXLAN
AS65xx0 (SDN Network)
AS65yy0 (SDN Network)
AS65zz0 (SDN Network)

## Slide 47: Configuration Requirements
You are running an AS65xx0 and announcing prefixes
  172.16.x.0/24.
  2a0b:4e07:c4:xx::/64
You help to transit prefixes announced by AS65xx1
  172.17.x.0/24.
  2a0b:4e07:c4:1xx::/64
IXP is AS65000 at 192.168.70.253/24 and fd70::fe/64
  You have to announce the prefixes you know to the IXP
  You can connect the IXP via
    192.168.70.x/24
    fd70::x/64
  BGP Password is winlab.nycu

## Slide 48: OVS and VXLAN
You can consider OVS as a bridge.
  You can create veth pairs and connect your container
  You can create VXLAN Tunnel
Let’s see if we can create a tunnel using `ovs-vsctl` and `ip` commands.
TA Server have already opened a VXLAN connection with IP 192.168.100.2/24
Dummy NIC
Veth
OvS
Veth
192.168.100.1/24
OvS
Veth
Dummy NIC
Veth
192.168.100.2/24
OvS
VXLAN
VXLAN
Veth
192.168.100.1/24
Dummy NIC
Veth

## Slide 49: OVS and VXLAN (cont.)
Create a ovs switch named br-ta
Set ovs protocol
Set ovs controller
Create a VXLAN port name TO_TA_VXLAN on ovs swtich br-ta
Set VXLAN connected to IP

## Slide 50: OVS and VXLAN (cont.)
You can use docker to create an onos controller
If you have finish lest step, you shall see two switches connected

## Slide 51: OVS and VXLAN (cont.)
You can see ports on the onos GUI that TA have created for you.
VLAN Port
OVS
Veth
Dummy NIC
Veth
192.168.100.2/24
OVS
VXLAN
VXLAN
Veth
192.168.100.1/24
Dummy NIC
Veth
A Veth for dummy NIC
Connect to AS65000
eth0
Connect to AS65000

## Slide 52: Topology Template
AS65xx0
ONOS
VXLAN
AS65xx1
Host 2
172.17.xx.1/24
2a0b:4e07:c4:1xx::1/64
172.17.xx.2/24
2a0b:4e07:c4:1xx::2/64
OVS1
OVS2
OVS3
192.168.100.1/24
VXLAN
FRRouting
192.168.63.2/24
fd63::2/64
192.168.60.xx/24
192.168.61.xx/24
AS65000
172.16.xx.2/24
2a0b:4e07:c4:xx::2/64
Host 1
192.168.70.253/24
fd70::fe/64
192.168.63.1/24
192.168.70.xx/24
172.16.xx.69/24
192.168.100.3/24
fd63::1/64
fd70::xx/64
2a0b:4e07:c4:xx::69/64
1Gbps Rate Limit
Also FRRouting
TA

## Slide 53: Sample Topology (x=3)
AS65030
ONOS
VXLAN
AS65031
Host 2
172.17.3.1/24
2a0b:4e07:c4:103::1/64
172.17.3.2/24
2a0b:4e07:c4:103::2/64
OVS1
OVS2
OVS3
192.168.100.1/24
FRRouting
192.168.63.2/24
fd63::2/64
192.168.60.3/24
192.168.61.3/24
AS65000
172.16.3.2/24
2a0b:4e07:c4:3::2/64
Host 1
192.168.70.253/24
fd70::fe/64
VXLAN
192.168.63.1/24
192.168.70.3/24
172.16.3.69/24
192.168.100.3/24
fd63::1/64
fd70::3/64
2a0b:4e07:c4:3::69/64
1Gbps Rate Limit
TA

## Slide 54: Sample Topology (x=25)
172.17.25.1/24
2a0b:4e07:c4:125::1/64
To avoid misconfiguration, don’t use a-f as IP in your settings.
  Use 25, instead
AS65250
ONOS
VXLAN
AS65251
Host 2
172.17.25.2/24
2a0b:4e07:c4:125::2/64
OVS1
OVS2
OVS3
192.168.100.1/24
FRRouting
192.168.63.2/24
fd63::2/64
192.168.60.25/24
192.168.61.25/24
AS65000
172.16.25.2/24
2a0b:4e07:c4:25::2/64
Host 1
192.168.70.253/24
fd70::fe/64
192.168.63.1/24
192.168.70.25/24
172.16.25.69/24
192.168.100.3/24
fd63::1/64
fd70::25/64
2a0b:4e07:c4:25::69/64
1Gbps Rate Limit
TA

## Slide 55: Review of Labs
Lab2
  ONOS API
  Flow rules
Lab3
  Mac learning
  Proxy ARP
Lab4
  Intent
  Meter Table
Lab5 Network Function Virtualization
  Simulate Autonomous Systems (AS)

## Slide 56: vRouter TODO List
Create a VXLAN tunnel between your SDN network and TA’s server.
ONOS can control OVS.
Adding IPV6 capability.
Intra domain packet handling.
  Make sure everything works fine within intra domain traffic.
Virtual Gateway function.
Edge routers can ping each other
  Since FRRouting is not directly connect to external router.
FRRouting can push FIB to ONOS controller.
  (Connection between 192.168.100.1 and 192.168.100.3)
Deal with inter-domain traffics, i.e. ASx’s hosts can ping ASy’s hosts.
Deal with transit traffics, i.e. ASx’s hosts can ping from outside the world.

## Slide 57: APP Configs
Recommended configs
{

## Slide 58: SDN AS Requirements
For service customers (AS65xx0 SDN Network, host 1)
  Able to ping FRRouting’s IP (172.16.xx.69/24).
  Able to ping student y’s FRRouting’s IP (172.16.yy.69/24).
  Use https://tools.keycdn.com/ipv6-ping to see ICMP replies.
For transit ISP (AS65xx1, host 2)
  Able to ping host 1 IP (172.16.xx.2/24).
  Able to ping student y’s FRRouting’s IP (172.16.yy.69/24).
  Able to ping student y’s host 2’s IP (172.17.yy.2/24).
  Use https://tools.keycdn.com/ipv6-ping to see ICMP replies.

## Slide 59: SDN Requirements
You can see what you have announced via IXP Manager
http://140.113.60.171:8880/lg
Your ASN
Your x
Click to see what you have announced
Choose IPv6 or IPv4

## Slide 60: SDN Requirements
You can see that you have connected to the outside world
https://tools.keycdn.com/ipv6-ping

## Slide 61: OUTLINE
Review of Labs
Virtual Router Explained
Virtual Router Specification
ONOS App and Services in Use
In Used App Configurations
Virtual Router Workflow
Supplement
Scoring Criteria
Reference

## Slide 62: Helper Scripts
There is a utils_topo.sh that might help you to create your topologies.
  Use brctl for building linux network bridges
  Use ovs-vsctl for building ovs bridges
Hints
  Remember to use your old project codes
  ONOS might have bugs due to it has not been updated for 2 years
    Use wireshark to make sure that the packet is exactly what you expected
    Print debug is your best friend
    Read the docs
  You can turn reactive forward to test your topologies

## Slide 63: TA Contacts
If you have any problem
  Mail to me
  Register demo time for help
Final Project
  Team Register (should be done before 12/5, update at everyday noon)
  https://docs.google.com/spreadsheets/d/18jBtdl7BgK_GIqJtgEI210icpPq_Et1tVk8eLnFe6Kk/edit?usp=sharing
  Demo Register https://calendar.google.com/calendar/u/0/appointments/AcZssZ2sbtt-446xWK_xPxxIv22bY-FV947i-odtBV4=
    Deadline: 12/31

## Slide 64: OUTLINE
Review of Labs
Virtual Router Explained
Virtual Router Specification
ONOS App and Services in Use
In Used App Configurations
Virtual Router Workflow
Supplement
Scoring Criteria
Reference

## Slide 65: Deployment Requirements
DO NOT TRY TO ATTACK EITHER OTHER STUDENTS OR TA SERVERS
You are required to create a Makefile so that you are able to
  Clear the entire project via make clean command
  Deploy the project via make deploy command
Only openflow (and route service) related apps can be use
If not, you will be scored 0

## Slide 66: Scores
Intra-domain traffic (from both AS)
  IPv4 (6 points)
  IPv6 (4 points)
Inter-domain traffic (from both AS)
  IPv4 (18 points)
  IPv6 (12 points)
Transit traffic
  IPv4 (18 points)
  IPv6 (12 points)
Routes shown in IXP Manager
  IPv4 (12 points)
  IPv6 (8 points)
Able to communicate with the outside world (10 points)

## Slide 67: OUTLINE
Review of Labs
Virtual Router Explained
Virtual Router Specification
ONOS App and Services in Use
In Used App Configurations
Virtual Router Workflow
Supplement
Scoring Criteria
Reference

## Slide 68: Reference
RouteService (https://javadoc.io/doc/org.onosproject/onos-cli/1.8.1/org/onosproject/incubator/net/routing/package-summary.html)
ONOS Java API (2.7.0) (https://api.onosproject.org/2.7.0/apidocs/index.html)
ovs-vsctl(8) - Linux manual page (https://man7.org/linux/man-pages/man8/ovs-vsctl.8.html)
ip(8) - Linux man page (https://linux.die.net/man/8/ip)